## Slide 1
MES WADIA COLLEGE OF ENGINEERING × ROBOCLUB (TEAM PLUTON)
PLUTO
ROBODOG · QUADRUPED PLATFORM
A voice-commanded, 12-servo quadruped built as a modular student platform for remote inspection and reconnaissance, with the human always in the loop.
Aryan Pawar · Unmesha Dasgude
MES Wadia College of Engineering
Virtual Robotics Project Presentation Competition
Notes: ARYAN: Good morning, everyone. We are Team PLUTON from ROBOCLUB, MES Wadia College of Engineering. I am Aryan Pawar. UNMESHA: And I am Unmesha Dasgude. Today we present PLUTO, also called RoboDog: a 12-servo quadruped robotics platform we built as a serious engineering base for remote inspection. We will show what works today, and clearly mark what we propose next.

## Slide 2: SOME PLACES ARE HARD TO SEE INTO
01 PROBLEM
Some places are too tight , too risky , too urgent to just walk into
Sending a person only to look can be dangerous
Confined, hazardous or time-critical spaces are hard to assess from the outside.
Sending a person in just to look is risky and could be fatal sometimes
The real issue is of human life risk which
01
NARROW PATCHES
Narrow or enclosed spaces that are awkward for a person to enter and look around.
02
HAZARDOUS
Conditions that are uncertain or unsafe to check in person.
03
INACCESSIBLE ZONES
Decisions that need a view of the situation quickly.
04
UNKNOWN
No picture of the space until someone is already inside it.
--------------------------------------------------------
Notes: ARYAN: Think about spaces where it is risky, slow or impractical for a person to go first: confined industrial areas, damaged infrastructure, sites after an incident. UNMESHA: In each case the real problem is information. People must decide what to do, but they decide without knowing what is ahead. Sending a person in just to look is often the most costly way to learn.

## Slide 3: A ROBO SCOUT THAT GOES FIRST
02 NEED
A robot can go first and report back while the human stays in charge.
The need is to extend human reach, not to replace human judgement.
The operator commands, the robot moves, and what it observes returns to the human.
The human interprets it and chooses the next command.
Observation and information return depend on proposed upgrades.
OPERATOR
COMMAND
ROBOT
MOVES
OBSERVE AND ANALYSE
INFORMATION
RETURNED
HUMAN
DECISION
NEXT
COMMAND
CURRENT
PROPOSED (PHASE 2)
The loop repeats. The human always interprets and decides.
Notes: UNMESHA: What is needed is a way to extend human reach. The robot goes first and reports back. ARYAN: Our philosophy is strict human-in-the-loop. The operator sends a command, the robot moves, something is observed and information comes back, and then the human decides the next command. The robot never decides for us. Observation and information return are what our proposed upgrades will add.

## Slide 4: LEGS: A CHOICE WITH A COST
03 WHY QUADRUPED
Individual foot placement is the gain; greater complexity is the price.
Wheels are simpler and efficient on smooth ground.
Legs place each foot individually,which allows flexibility
We chose legs as an engineering challenge and a base for future work.
WHEELS
Limited movement on rough terrain.
Easier to control and calibrate
Needs continuous ground contact
Well suited to smooth ground
Can slip on uneven surfaces.
LEGS (PLUTO)
Each foot placed individually
12 actuators to coordinate
Rough-ground use is a future goal, not demonstrated
Can step over obstacles.
Flexible movement.
Allows different walking patterns
TRADE-OFF: placement control ↔ complexity
Notes: ARYAN: We want to be honest here. Wheels are simpler, and on smooth ground they are hard to beat. UNMESHA: Legs trade simplicity for individual foot placement: each foot lands where the controller chooses rather than rolling continuously. For PLUTO that means 12 actuators to coordinate and more to calibrate. We chose it as an engineering challenge and as a base for future rough-ground work, which is a proposal, not something we have demonstrated.

## Slide 5: WORKING BEHIND THE VOICE COMMANDS
04 TECHNICAL DESIGN
A short control chain turns one spoken command into coordinated movement.
A predefined voice command is recognised by the VC02 and passed to the Arduino Uno.
The Arduino sends servo targets over I²C to the PCA9685, which drives all 12 servos.
The result is a programmed action: stand, sit, walk, bow or handshake.
VOICE
COMMAND
Predefined phrase
VC02
Recognises it
ARDUINO
UNO
Runs the routine
PCA9685
Drives servos
12
SERVOS
Move the joints
I²C
INPUT
VC02 hears a fixed set of commands
VC02 is pre-trained model which include fixed set of commands
CONTROL
The Arduino holds stored sequences of joint positions and timing, and picks one to run when VC02 sends signal
ACTUATION
The PCA9685 distributes PWM to 12 channels so all joints move in step.
joint movement → robot action. Command-driven and programmed;.
Notes: UNMESHA: This is the whole control chain. A voice command is picked up by the VC02 module. It tells the Arduino Uno which routine to run. The Arduino talks over I2C to the PCA9685 servo driver, which drives all 12 servos. Joints move, and the robot performs the action. ARYAN: Each block has one clear job, which keeps the system understandable and easy to extend.

## Slide 6: THE CHALLENGE IS COORDINATION
05 12-DOF PLATFORM
Moving one motor is easy; moving twelve in step was the engineering challenge.
PLUTO has four legs with three servo-driven joints each.
Every step needs all 12 joints at the right position at the right time.
Routines are stored as joint positions with timing, so calibration directly affects how well the robot moves.
FRONT
LEFT FRONT
JOINT 1
Hip servo
JOINT 2
Shoulder servo
JOINT 3
Ankle servo
3 servo channels
RIGHT FRONT
JOINT 4
Hip servo
JOINT 5
Shoulder servo
JOINT 6
Ankle servo
3 servo channels
LEFT BACK
JOINT 7
Hip servo
JOINT 8
Shoulder servo
JOINT 9
Ankle servo
3 servo channels
RIGHT BACK
JOINT 10
Hip servo
JOINT 11
Shoulder servo
JOINT 12
Ankle servo
3 servo channels
BACK
4 legs × 3 joints = 12 servos on 12 of the 16 PCA9685 channels
[Confirm] joint names -Hip , Shoulder, Ankle
Servo model-20KG.cm Servo motors- DS3218
Notes: ARYAN: PLUTO has four legs with three servo-driven joints each, so twelve degrees of freedom in total. UNMESHA: Any single servo is simple. The difficulty is that every step needs all twelve joints to be at the right position at the right time. That is why our motion routines are stored as joint positions with timing, and why calibration matters. Joint names are still being confirmed by the team.

## Slide 7: THREE PARTS, THREE CLEAR JOBS
06 CONTROL ELECTRONICS
Each module is simple, off the shelf and replaceable.
The Arduino Uno holds the routines and decides what runs.
The PCA9685 generates the servo signals so the controller does not have to.
The VC02 recognises only a fixed set of predefined commands.
ARDUINO UNO
MAIN CONTROLLER
Stores motion routines
Selects a routine on command
Sends servo targets over I²C
Accessible and well understood
PCA9685
16-CHANNEL PWM DRIVER
I²C link to the Arduino
Drives all 12 servos
Offloads PWM generation
4 channels spare
AI THINKER VC02
VOICE MODULE
Fixed, predefined commands
Triggers the Arduino
No language understanding
Easy to make changes in voice commands
Notes: UNMESHA: The Arduino Uno is the main controller. It holds the motion routines and decides which one to run. We chose it because it is accessible and well understood, which suits a student platform. ARYAN: The PCA9685 generates the servo signals for up to 16 channels over I2C, so the Arduino does not have to. The VC02 recognises a fixed set of predefined voice commands. It is not conversational, and we do not claim that it is.

## Slide 8: WALKING IN DIAGONAL PAIRS
07 WALKING GAIT
A programmed gait alternates two diagonal leg pairs across all 12 channels.
Left Front and Right Back swing together, then Right Front and Left Back.
While one pair swings, the other pair is on the ground.
A programmed sequence of joint positions and timing on controlled surfaces; it can be calibrated through code in Arduino
PHASE A
PHASE B
LEFT FRONT
SWING
ON GROUND
RIGHT BACK
SWING
ON GROUND
RIGHT FRONT
SWING
ON GROUND
LEFT BACK
SWING
ON GROUND
one gait cycle
TOP VIEW
LF
RF
LB
RB
LF
RF
LB
RB
Notes: ARYAN: Walking uses an alternating diagonal gait. Left Front and Right Back move together, then Right Front and Left Back. UNMESHA: While one diagonal pair swings forward, the other pair is on the ground. The bars show this timing. It is a programmed sequence of joint positions and timing on a controlled surface. It is not an adaptive gait, and we have no balancing or terrain sensing today.

## Slide 9: PRESENTING PLUTO: A SCOUT BOT
08 WORKING PROTOTYPE
A built, working Phase 1 platform with voice-triggered motion routines.
Four legs, 12 servos and a 3D-printed structure, controlled by an Arduino Uno.
Five programmed routines run as stored joint positions and timing.
For power we used battery with 16 channel PCA to run the motors
Here each leg having 3 degrees of freedom
35.5 cm [confirm]
30 cm
[Insert photo: PLUTO full robot]
width 22 cm [confirm]
MOTION ROUTINES
STAND
SIT
WALK
BOW
HANDSHAKE
Notes: ARYAN: This is the current prototype: four legs, twelve servos, a 3D-printed structure and an Arduino Uno as the controller. UNMESHA: It performs five programmed routines: stand, sit, walk, bow and handshake. Each is a stored sequence of joint positions and timing. We have not measured speed, payload or battery life, so we do not quote numbers. The dimensions on screen are still to be confirmed.

## Slide 10: TURNING COMMAND TO MOTION
09 DEMONSTRATION
The prototype running its routines on a controlled surface.
Watch the chain in action: a spoken command, recognition by the VC02, then the matching routine on all 12 joints.
These are programmed motions, not decisions made by the robot.
WHAT TO WATCH
COMMAND
SPOKEN
VC02
RECOGNISES
ARDUINO
RUNS ROUTINE
12 JOINTS
MOVE
Notes: UNMESHA: Here is the prototype responding to its predefined voice commands. ARYAN: Watch for the sequence: a command is spoken, the VC02 recognises it, and the robot performs the matching routine. These are programmed motions, not decisions made by the robot. [Play demo video here.]

## Slide 11: PROPOSED: GIVE PLUTO SENSES
10 PURPOSEFUL UPGRADE
Each module adds one piece of information the human operator needs.
Everything here is proposed and not installed.
Camera, proximity sensing, LED illumination, temperature sensing and a wireless link would let the robot report back.
A Raspberry Pi comes later for processing and vision. Modules can be added one at a time.
PROPOSED · NOT INSTALLED
CAMERA
Lets the operator see the space
PROXIMITY SENSING
Detects nearby objects
LED ILLUMINATION
Lights dark areas for the camera
VARIOUS SENSORS
Reports conditions to the operator
Sensors can be modified according to its applications
WIRELESS LINK
Returns video and sensor data
Through Internet or it will be stored and then later on analyse
RASPBERRY PI (LATER)
Processing, sensor fusion, vision, obstacle awareness, adaptive gait
PROPOSED DATA PATH
CAMERA +
SENSORS
WIRELESS
LINK
OPERATOR
(HUMAN)
Notes: ARYAN: Everything on this slide is proposed. None of it is installed today. UNMESHA: A camera and LED illumination would let the operator see. Proximity sensing and temperature sensing add other readings. A wireless link would carry video and sensor data back. Later, a Raspberry Pi could handle processing, sensor fusion and computer vision. A camera could connect through that link, and the platform is modular so we can add one module at a time.

## Slide 12: WHERE IT COULD BE USEFUL
11 APPLICATIONS
Each use is a potential future one and depends on a named upgrade.
These are directions, where PLUTO can be useful in future.
Each use needs the upgrades named on its card.
In every case the operator remains the decision-maker.
This will help reducing human risk factor
POTENTIAL FUTURE USE
INDUSTRIAL INSPECTION
Look into machinery areas before a person goes in
NEEDS: Camera, LED illumination
POTENTIAL FUTURE USE
SECURITY SURVILLIENCE
Will help large campuses in surveillance and could also help in defense sectors
NEEDS: Camera, LED, proximity sensing
POTENTIAL FUTURE USE
POST-DISASTER RESCUE
This bot will be a efficient option to search and rescue people after a disaster
NEEDS: Camera, wireless link
POTENTIAL FUTURE USE
EXPLORATION
Survey unfamiliar spaces and report back
NEEDS: Camera, proximity sensing, wireless link
POTENTIAL FUTURE USE
ENVIRONMENTAL MONITORING
Collect conditions at a location and is very helpful for farmers in their farms
NEEDS: Temperature sensing, wireless link
SPACE EXPLORATION
Have potential applications in space exploration, assisting in planetary exploration missions, such as on Mars or other celestial bodies
Notes: UNMESHA: These are potential future uses, not current capabilities. Each card names the upgrade it would need. ARYAN: For example, infrastructure inspection would need the camera and lighting. Environmental monitoring would need temperature sensing and a wireless link. Today PLUTO can do none of these tasks, and we do not claim otherwise.

## Slide 13: REALISTIC BECAUSE IT IS INCREMENTAL
12 FEASIBILITY
The plan rests on what already works and on challenges we state openly.
Locomotion and voice control already work.
Upgrades are modular, and human-in-the-loop operation means full autonomy is not required.
The open challenges are real and shape our next steps.
WHAT IS TRUE TODAY
Locomotion works
Voice control works
Upgrades are modular and incremental
Human-in-the-loop: full autonomy not required
HONEST CHALLENGES
Servo power demand
Mechanical reliability and calibration
Environmental protection
Communication range
ADD ONE MODULE AT A TIME → TEST → THE HUMAN DECIDES
Notes: ARYAN: Feasibility rests on what is true. Locomotion and voice control already work. The upgrades are modular, so we add them one at a time. And because a human stays in the loop, full autonomy is not required. UNMESHA: The challenges are honest ones: servo power demand, mechanical reliability and calibration, protecting the electronics from the environment, and communication range. We plan to address them phase by phase.

## Slide 14: THREE PHASES, ONE DIRECTION
13 ROADMAP
Capability grows step by step, and the human stays in the loop throughout.
Phase 1 is complete and demonstrable.
Phase 2 is proposed and adds sensing and communication.
Phase 3 is future research toward semi-autonomy; the operator still decides.
CURRENT
PHASE 1
MOBILITY AND CONTROL
12-servo quadruped
Voice-commanded routines
Alternating diagonal gait
PROPOSED
PHASE 2
SENSING AND COMMUNICATION
Camera and LED illumination
Proximity and temperature sensing
Wireless video and data link
FUTURE RESEARCH
PHASE 3
PERCEPTION AND SEMI-AUTONOMY
Raspberry Pi processing
Sensor fusion and computer vision
Obstacle awareness, adaptive gait
Notes: UNMESHA: Phase 1, Mobility and Control, is current: the platform you have just seen. ARYAN: Phase 2, Sensing and Communication, is proposed: camera, proximity, LED, temperature and a wireless link. Phase 3, Perception and Semi-Autonomy, is future research with a Raspberry Pi. Even then, the human decides.

## Slide 15
14 CLOSING
PLUTO EXTENDS HUMAN REACH
Human decides Bot acts…
The innovation: voice interaction, 12-actuator coordination and embedded control, together on a modular platform
A quadruped robot works on voice commands
Next: sensing and communication (proposed)
MODULAR
platform
COORDINATED
12-joint motion
CLEAR PATH
human in the loop
THANK YOU !!
Notes: ARYAN: To close: PLUTO is a working 12-servo quadruped platform, built to extend human reach while the human keeps the decisions. UNMESHA: Our contribution is not inventing quadruped robotics or voice recognition. It is integrating voice interaction, 12-actuator coordination and embedded control on a modular platform. Next, we plan to build sensing and communication. Thank you. We are happy to take your questions.